## Slide 1
—Power Unit Problem Solving
—Display Unit Problem Solving
—Audio Unit Problem Solving
—Functional Unit Problem Solving
CV9202H-UPW-11
Common problems solution

## Slide 3
In stand-by condition,
Check pin 4，5，6 of J10,
Whether got +12V？
Normal booting
Whether power suppply and main board is short circuit?
Whether power chip LDO(U12) works?
power chip DC (U8,U9) works? Check DIODE (D5)work？
After power on, check testing point TP7 got 3.3v, testing point D5 got 2.5v, testing Point TP5 got 1v? Testing Point TP6 got 1.5v?
Picture 1: Power Units Problem Solving
(Mainboard can not boot)
Y
N
OK
Check the DC(U9)，LDO(U17) related devices
N
Y
Y
N
Check external power suppply
Whether main board
testing point TP8 got 5V_SB? TP9 got 3.3_SB?

## Slide 4
Black screen
Whether the voltage that
power panel supply
is normal?
Check the socket that controls Inverter,
whether the voltage output from pin 1 of J10
is in high level?
Check the external power supply circuit
N
N
Y
Y
Check and repair the
network that controls
Inverter ON/OFF
Inverter is broken or
connecting line is not good
Picture 2
Display unit ( black screen)

## Slide 5
Mess or
Black screen（Back light on）
Whether driven board cable is correct?
connection is Ok?
Check whether it is OK
after changing LCD?
Y
N
N
Y
Check output network,
Whether
J15 driven board
socket part is normal?
Y
Check whether
U15
power supply and
clock circuit chip LVDS
output pin is short ciucuit
or open circuit?
Repair this circuit
N
Whether LCD power VCC-Panel is correct? Voltage in pin 1 or 2 of J15 is correct? Q3 output voltage is correct?
Whether the software
matches?
Upgrade the
matched software
again
N
Change driven board
cable
Change LCD
Picture3
Display unit(mess)

## Slide 6
No sound
If there is anyaudio signal input
or Whether amplifier power supply
is normal?
Check
peripheral
audio
equipment:
amplifier
power
supply
circuit
Whether there is signal
input in
U16（tpa3110）pin 3/12?
N
Y
Y
N
Whether the volume,
MUTE
setting is normal?
Resetting
Whether there is
signal output from J13?
Y
N
Check
external
loudspeaker
N
Y
Check and repair
network
of the connecting
part between
U14 and U16
Picture 4
Audio part (no sound)
Check and repair
amplifier power supply
circuit, if power supply
is normal, then change U16

## Slide 7
Picture 5
Function unit (ATV video broke down)
Check whether
external RF input signal
is normal?
N
Y
Check whether pin2
of tuner U21 got 3.3V?
Check and repair power supply FB10
network
Y
N
Check pin9,10of tuner U21,
whether there is I2C data?
Check whether I2C network pull-up voltage is normal?
N
Y
Whether pin 5、6 of U21
got intermediate-frequency signal?
N
Repair the connecting circuit
Y
Whether t he peripheral circuit
of U21 is normal?
N
Y
Repair the peripheral circuit
N
Y
Check video sound meter U14 circuit connecting network
Change tuner
Whether the direct connecting network of U14 is normal?
Check and
repair
peripheral
RF
equipment
TV no searching
/no image

## Slide 8
TV no sound, only picture
Whether there is
sound under PC/AV？
N
Y
Refer to “NO SOUND”
repair guide
Picture 6
Function unit (ATV/DTV no sound)
Change U14
Whether software is OK? input system is set correctly?

## Slide 9
Under PC
Image not
in the middle
Miss color,
Color
cast
Image
shakes
No signal
Carry out
auto-adjust
operation
Whether U14
R.G.B input signal is normal?
The system
setting
is incorrect,
reset it
Y
N
Whether VS,HS signal
is regular or stable?
Check VS.HS
circuit
OSD setting
doesn’t match,
reset it,
or input mode
doesn’t support
Check VS.HS
circuit
Y
N
Whether the
contact of
VGA socket
is good?
Whether the
contact of
VGA socket
is good?
Check VGA
input circuit
Picture 7
Function unit（PC）

## Slide 10
Under HDMI
No image
There is image
but no sound
Refer to "power failure"
repair guide
Check HDMI and input network
Check HDMI
input network
and EDID
Check HDMI related network of U14
N
Picture 8
Function unit（HDMI）
Whether there is
sound under PC?
Y
N
Refer to "no sound" repair guide
Y
Whether HDMI
contact
is good?

## Slide 11
TV no searchin/no image
Picture 9
Function unit(DVB-S2 video breakdown)
Whether external RF
input signal is normal?
N
Check and
repair
peripheral
RF equipment
Y
Check whether pin 23,28
of U3 got 3.3V?
Check and repair the power supply network FB5 circuit of this pin
Y
N
U3 is broken, change tuner
N
Y
Check whether there is
TS signal output from U2?
N
Check whether the connection from U2 to U14 is OK?
Y
U2 is broken, change demo
N
Y
Check U14
peripheral circuit
Check pin 8,9 of tuner U3,
whether there is IQ signal?
Check and repair
this connecting circuit